## Slide 1: Design of Digital Circuits Lab 4 Supplement: Finite State Machines
Prof. Onur Mutlu
ETH Zurich
Spring 2019
26 March 2019

## Slide 2: What Will We Learn?
In Lab 4, you will implement a finite state machine using Verilog.
Design and implement a simple circuit that emulates the blinking lights of a Ford Thunderbird.
Understand how the clock signal is derived in the FPGA board.
Write an FSM that implements the Ford Thunderbird blinking sequence.

## Slide 3: Tail Lights of a 1965 Ford Thunderbird
In this lab, you will design a finite state machine to control the tail lights of a 1965 Ford Thunderbird.

## Slide 4: Tail Lights of a 1965 Ford Thunderbird
There are three lights on each side that operate in sequence to indicate the direction of a turn.
Copyright from ClassicLEDs.com

## Slide 5: Part 1: FSM Design
The job of an FSM is to do three things:
  Next State Logic: Determine the next state from the present state and the inputs.
  Output Logic: If a Mealy FSM is used, realize the output function based on the present state and the input.
  State Register: Advance from the present state to next state when a clock event arrives.
  Note: The manual contains the details of this FSM specifications.

## Slide 6: Part 1: FSM Design
The job of an FSM is to do three things:
  Next State Logic: Determine the next state from the present state and the inputs.
  Output Logic: If a Mealy FSM is used, realize the output function based on the present state and the input.
  State Register: Advance from the present state to next state when a clock event arrives.
  Note: The manual contains the details of this FSM specifications.
For more details on FSM designs (Mealy vs. Moore) please refer to lecture 7.1, slide 13:
Link

## Slide 7: Part 2: Verilog Implementation
Separate three parts of the code:

## Slide 8: Part 2: Verilog Implementation
Separate three parts of the code:

## Slide 9: Part 2: Verilog Implementation
Separate three parts of the code:

## Slide 10: Part 4: Implementing the Clock (I)
The problem of using push-bottons as clock:
  Compared to the speed of the FPGA the change in a push button is very very slow (1million x)
  During the slow transition, the FPGA will see many fast occurring transitions and would interpret each of them as a clock edge. (Bouncing)

## Slide 11: Part 4: Implementing the Clock (II)
CLK100Mhz (W5): Your board contains a 100Mhz crystal oscillator circuit.
Problem: The clock is too fast.
Solution: A clock divider:

## Slide 12: Part 4: Defining the Constraints
Buttons for control
LEDs for output lights
Connections for clock

## Slide 13: Last Words
In Lab 4, you will implement a finite state machine using Verilog.
Design and implement a simple circuit that emulates the blinking lights of a Ford Thunderbird.
Understand how the clock signal is derived in the FPGA board.
Write an FSM that implements the Ford Thunderbird blinking sequence.
In the report, you will implement a dimming function, so that the lights are not only on and off, but can have intermediate levels

## Slide 14: Design of Digital Circuits Lab 4 Supplement: Finite State Machines
Prof. Onur Mutlu
ETH Zurich
Spring 2019
26 March 2019